## Slide 1: Flow Shop Scheduling

## Slide 2: Scheduling - Single Stage
Consider a set of jobs which need to be processed by a single machine/stage/activity.
e.g. a supermarket queue at one checkout.
Makespan – Total time taken to process all jobs
Completion Time – the time at which a job is finished: its waiting time in the queue plus its own processing time.
e.g. You are buying a Kit-Kat and are behind someone with a full trolley.
If they are kind enough to let you through, what happens to the Makespan and the Completion Time ?
Makespan isn’t concerned with order. The checkout takes the same amount regardless of order.
Completion Time however is vastly different. If you are not let by, you both wait for almost the entire Makespan.

## Slide 3: Shortest Processing Time
Consider a set of jobs which need to be processed by a single machine (stage).
e.g. a supermarket queue at one checkout.
- Makespan, i.e. the last completion time
- Completion time of job
- Sum of all completion times (total completion time).
- length of job
Shortest processing time, order the jobs in ascending order

## Slide 4: Shortest Processing Time
Lemma 1: Let be a vector of descending order and a vector of the same length of no specific order. The minimum scalar product of occurs when is of ascending order.
Proof:
Such that:
Assume we have two indices (not necessarily adjacent) such that:
Define a new vector where these two elements are swapped.

## Slide 5: Shortest Processing Time
But and
Thus, swapping any two elements in where results in an equal or lower scalar product

## Slide 6: Shortest Processing Time
Therefore, for any not in ascending order, there exists a swap which results in an equal or lower scalar product .
Thus, the minimum is attained when is in ascending order.

## Slide 7: Shortest Processing Time
Theorem: SPT is optimal for minimising the sum of completion times
Proof:
is of descending order, therefore, to obtain a minimum by the previous lemma needs to be of ascending order, i.e. shortest processing time first.

## Slide 8: Flow Shop Scheduling
We will deal with a simpler set up than the general job shop scheduling problem.
Often a company will have multiple jobs (e.g. products) that go through multiple stages (machines) sequentially.
Each job may require a different amount of time at each stage.

## Slide 9: Example
A
B
Consider a 2 stage process in sequence.
Each job requires different times at each stage.
e.g.
Start Job
End Job
Job Processed at Stage 1
Job Processed at Stage 2

## Slide 10: Example
Schedule jobs in order they appear. PQR
Is this optimal for Makespan? i.e. is everything completed as quickly as possible?
No PRQ

## Slide 11: Makespan and Idle Time
Makespan is the total time required to complete all jobs
Idle Time is the time a stage (machine) is idle.
Stage A is idle for 6 units of time.
Stage B is idle for 2+3=5 units of time.

## Slide 12: Optimality
Optimality is difficult to check! These are NP-Hard problems
How many possible permutations? No repetitions and order matters!
P
Q
R
Q
R
R
P
Q
P
R
Q
R
P
Q
P
OR
For jobs there are ways of scheduling.
e.g. jobs,

## Slide 13: Johnson’s Rule
Minimises Makespan
Optimal solution for 2 stages (machines)
Optimal solution for 3 stages (machines) given additional conditions
  Not covering this…
Everything else is NP-hard
In general problems like these require clever guessing (heuristics)
It effectively schedules the jobs which are small for the first stage at the beginning, and those that are small for the second stage at the end.
https://www.rand.org/content/dam/rand/pubs/papers/2008/P402.pdf

## Slide 14: Johnson’s Rule (Two stage)
Steps
  List the jobs
  Select the job with the shortest activity time, break ties arbitrarily
    If shortest is for first stage, schedule as early as possible
    Else if shortest is for second stage, schedule as late as possible
  Remove the job from list.
  Repeat 2 and 3 until no jobs are left to schedule

## Slide 15: Example
Metric | Time
Makespan | 40
Idle Time of A | 16
Idle Time of B | 11
Total Idle Time | 27
Before applying Johnson’s Rule

## Slide 16: Example
  List the jobs
  Select the job with the shortest activity time, break ties arbitrarily
    If shortest is for first stage, schedule as early as possible
    Else if shortest is for second stage, schedule as late as possible
  Remove the job from list.
  Repeat 2 and 3 until no jobs are left to schedule

## Slide 17: Example

## Slide 18: Example
Solution | Makespan | Idle Time of A | Idle Time of B | Total Idle Time
Original order | 40 | 16 | 11 | 27
Johnson’s | 30 | 6 | 1 | 7
After applying Johnson’s Rule

## Slide 19: Example 2
Solution | Makespan | Idle Time of A | Idle Time of B | Total Idle Time
Original order | 19 | 7 | 6 | 13

## Slide 20: Example 2
Solution | Makespan | Idle Time of A | Idle Time of B | Total Idle Time
Original order | 19 | 7 | 6 | 13
Johnson’s | 18 | 6 | 5 | 11

## Slide 21: More Than 2 Machines
Solution | Makespan | Idle Time of A | Idle Time of B | Idle Time of C | Idle Time of D | Total Idle Time
Original order | 52 | 29 | 25 | 30 | 27 | 111

## Slide 22: More Than 2 Machines
Johnson’s rule can be used to reduce the size of the search space.
Idea - reduce to a 2-stage problem. This is a heuristic!
  Only produces a good solution, not necessarily optimal!
  Often named the method/approach of Campbell, Dudek and Smith
e.g. First and last stage considered
Makespan - 46

## Slide 23: Other Possibilities
Aggregate the first two machines and last two machines
Aggregate the first three machines and last three machines
Makespan - 46
Makespan - 48

## Slide 24: For machines
possible sequences
Consider all these sequences and pick the best one!

## Slide 25: Trivia Time…
The average human body contains how many pints of blood?
9
The Statue of Liberty was given to the US by which country?
France
What title is shared by a 1983 Lionel Richie song and a 2015 Adele song?
Hello